Lotus Europa Federal S2 Brake Lines – Modified for Wilwood Hanging Pedal Assembly.

Brake Switch location is on the side of the chassis vs top.  See Picture 3 below.

|  |  | Termination Point A |  |  |  | Termination Point B |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Qty | Description | Size |  | Flare Type | Length | Size |  | Flare Type |
| 1 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 18" | 3/8"-24 | Female | Double Inv - OP.2 |
| 1 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 10" | 3/8"-24 | Female | Double Inv - OP.2 |
| 2 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 33" | 3/8"-24 | Female | Double Inv - OP.2 |
| 1 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 47" | 3/8"-24 | Female | Double Inv - OP.2 |
| 1 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 9" | 3/8"-24 | Female | Double Inv - OP.2 |
| 1 | Steel Brake Line | 3/8"-24 | Male | Bubble Flare | 82" | 3/8"-24 | Male | Bubble Flare |
| 2 | SS Braided Lines | 3/8"-24 | Male | Bubble Flare | 12" | 3/8"-24 | Male | Bubble Flare |
| 2 | SS Braided Lines | 3/8"-24 | Male | Bubble Flare | 15" | 3/8"-24 | Male | Bubble Flare |
| 8 | Jam Nuts | 3/8"-24 |  |  |  |  |  |  |

Picture 1. Male End

Picture 2. Female with Nut

Picture 3. Typical hose to line connection with out separate bulkhead fitting.  Note long male ends.

Note: 82” brake line is 3” shorter than stock due to Wilwood hanging pedal assy.

Doubt if these SS lines will be long enough to reach Wilwood Dynalite front calipers.  Likely will be replaced with longer lines with 90 degree fittings. (in process)